## Slide 1: STM32 Dist
Micro105

## Slide 2: Timing peripherals
WDGs (3.3)
  WWDG lab (3.3.1)
  IWDG lab (3.3.2)
3

## Slide 3: 5. BSP package
FMC SDRAM BSP lab (5.1)
LCD BSP Print text lab (5.2)
5

## Slide 4: 3.3.1 WWDG lab

## Slide 5: Use WWDG
Objective
  Learn how to setup WWDG in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple application to test WWDG
Goal
  Configure WDGin in CubeMX and Generate Code
  Learn how to start WWDG
  WWDG indication via LED
3.3.1

## Slide 6: Use WWDG
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX WWDG selection
  Select WWDG
  Configure PG14 for LED indication
3.3.1

## Slide 7: Use WWDG
In order to run on maximum frequency, setup clock system
Details in lab 0
3.3.1

## Slide 8: Use WWDG
CubeMX ADC configuration
  TAB>Configuration>System> >WWDG>Parameter Settings
  Set prescaller to 8
  WWDG window to 80
  And free running counter to 127
  Button OK
3.3.1

## Slide 9: Use WWDG
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
3.3.1

## Slide 10: Use WWDG
How calculate the window APB1freq=45MHz, prescaller 8
In our case 80
Fixed 63
We refresh the WWDG to 127
3.3.1

## Slide 11: Use WWDG
Solution
  WWDG Start
  WWDG refresh
/* USER CODE BEGIN 2 */
HAL_WWDG_Start(&hwwdg);
/* USER CODE END 2 */
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
//30ms or 50ms is outside the WWDG window, 40ms fits inside the window
HAL_Delay(40);
HAL_GPIO_WritePin(GPIOG, GPIO_PIN_14, GPIO_PIN_SET);
HAL_WWDG_Refresh(&hwwdg, 127);
}
/* USER CODE END 3 */
3.3.1

## Slide 12: 3.3.2 IWDG lab

## Slide 13: Use IWDG
Objective
  Learn how to setup IWDG in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple application to test IWDG
Goal
  Configure IWDG in CubeMX and Generate Code
  Learn how to start IWDG
  IWDG indication via LED
3.3.2

## Slide 14: Use IWDG
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX IWDG selection
  Select IWDG
  Configure PG14 for LED indication
3.3.2

## Slide 15: Use IWDG
In order to run on maximum frequency, setup clock system
Details in lab 0
3.3.2

## Slide 16: Use IWDG
CubeMX ADC configuration
  TAB>Configuration>System> >IWDG>Parameter Settings
  Set prescaller to 4
  Max value to 50
  Button OK
3.3.2

## Slide 17: Use IWDG
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
3.3.2

## Slide 18: Use IWDG
IWDG refresh interval
3.3.2

## Slide 19: Use IWDG
Solution
  IWDG Start
  IWDG refresh
/* USER CODE BEGIN 2 */
HAL_IWDG_Start(&hiwdg);
/* USER CODE END 2 */
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_Delay(7);//try delay 6ms and 7ms
HAL_GPIO_WritePin(GPIOG,GPIO_PIN_14,GPIO_PIN_SET);
HAL_IWDG_Refresh(&hiwdg);
}
/* USER CODE END 3 */
3.3.2

## Slide 20: Use IWDG
Hardware IWDG
  Remove IWDG start from project
  Use ST-Link utility and enable IWDG Hardware start
/* USER CODE BEGIN 2 */
/* USER CODE END 2 */
3.3.2

## Slide 21: Use IWDG
Hardware IWDG
  Start ST-Link utility
  Menu>Target>Option bytes or CTRL+B
  Uncheck the WDG_WS
  Button APPLY
  Now the IWDG is automatically started after reset
!!! DO NOT FORGET disable IWDG automatic start after you end this example
3.3.2
Notes: Check if it is functional

## Slide 22: 5.1 BSP SDRAM lab

## Slide 23: Use BSP for SDRAM initialization
Objective
  Learn how import BSP into project
  Which part need to by configured in GUI
  Try to write data into SDRAM and read it
Goal
  Successfully import BSP into your project
  Learn which part you need to import
  How to setup the project
5.1

## Slide 24: Use BSP for SDRAM initialization
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
We need only blank project with clock initialization
  We only set the RCC and configure the core to maximum speed
5.1

## Slide 25: Use BSP for SDRAM initialization
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
5.1

## Slide 26: Use BSP for SDRAM initialization
Now we have bank project
For SDRAM we need to include more parts
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
5.1

## Slide 27: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
5.1

## Slide 28: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
2. include stm32f4xx_discovery.h
1. include stm32f4xx_discovery_sdram.h
5.1

## Slide 29: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
3. include stm32f4xx_hal.h
stm32f4xx_hal.c
4. stm32f4xx_hal.h include all peripherals which are used in stm32f4xx_discovery.c
5.1

## Slide 30: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
5. stm32f4xx_hal.h include all peripherals which are used in stm32f4xx_discovery_sdram.c
5.1

## Slide 31: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
6. HAL_SDRAM_Init is function from stm32f4xx_discovery_sdram.c
7. HAL_SDRAM_Init
call functions from stm32f4xx_II_fmc.c
8. stm32f4xx_II_fmc.c use functions from stm32f4xx_hal_sdram.c
5.1

## Slide 32: Use BSP for SDRAM initialization
stm32f4xx_hal_ppp.h
stm32f4xx_hal_ppp_ex.h
stm32f4xx_hal.h
stm32f4xx_it.c
user_code.c
Source files
Include files
stm32f4xx_hal_def.h
stm32f4xx_hal_conf.h
stm32f4xx_hal_ppp.c
stm32f4xx_hal_ppp_ex.c
stm32f4xx_hal.c
HAL Drivers
User Code
user_code.h
stm32f4xx_it.h
BSP Drivers
Stm32f4xx_discovery.c
Stm32ffxx_discovery_sdram.c
Stm32f4xx_discovery.h
Stm32ffxx_discovery_sdram.h
5.1

## Slide 33: Use BSP for SDRAM initialization
The copy part
  In our project in Drivers folder create folder BSP
  Now go into CubeMX repository …\STM32Cube_FW_F4_V1.3.0\Drivers\BSP\
  And copy Components and STM32F429I-Discovery into BSP folder
Copy folders into BSP
5.1

## Slide 34: Use BSP for SDRAM initialization
Now we need to add this files also in project
  Create BSP folder in project
  Right click on project in Workplace>ADD>Group
  Name it BSP
  Now right click on BSP>ADD>Files
  From Drivers\BSP\STM32F429I-Discovery\ add stm32f429i_discovery.c and stm32f429i_discovery_sdram.c
5.1

## Slide 35: Use BSP for SDRAM initialization
The stm32f429i_discovery.c contains functions for all components on discovery kit (LCD, GYRO,…)
Then we also need add into project HAL library which handle their interface (I2C, SPI, … )
Right click on STM32F4xx_HAL_Drive>ADD from \Drivers\STM32F4xx_HAL_Driver\Src
  stm32f4xx_hal_i2c.c
  stm32f4xx_hal_spi.c
  stm32f4xx_hal_sdram.c
  stm32f4xx_II_fmc.c
5.1

## Slide 36: Use BSP for SDRAM initialization
Now add the include paths for this new files
  Right click on project>Options>Category C/C++Compiler>Preprocesor
  Into Defined symbols add USE_STM32F429I_DISCO
  This allow use BSP functions
  Into additional includes add $PROJ_DIR$\..\..\Drivers\BSP\STM32F429I-Discovery
  Button OK
  Button OK close project options
5.1

## Slide 37: Use BSP for SDRAM initialization
Now last thing is allow to include new HAL files which we added
  Open stm32f4xx_hal_conf.h in ..\Inc\
  Uncomment files which we added
  HAL_SDRAM_MODULE_ENABLED
  HAL_I2C_MODULE_ENABLED
  HAL_SPI_MODULE_ENABLED
5.1

## Slide 38: Use BSP for SDRAM initialization
Into main.c now we add include of stm32f429i_discovery_sdram.h
Now we can use the SDRAM init functions from BSP
Now you can try to write into SDRAM area In stm32f429i_discovery_sdram.h you can find where is the SDRAM memory and how is their size
  SDRAM_DEVICE_ADDR ((uint32_t)0xD0000000)
  SDRAM_DEVICE_SIZE ((uint32_t)0x800000) /* SDRAM device size in MBytes */
/* USER CODE BEGIN Includes */
#include "stm32f429i_discovery_sdram.h"
/* USER CODE END Includes */
/* USER CODE BEGIN 2 */
BSP_SDRAM_Init();
/* USER CODE END 2 */
5.1

## Slide 39: Use BSP for SDRAM initialization
SDRAM test
/* USER CODE BEGIN PV */
volatile uint32_t value;
/* USER CODE END PV */
/* USER CODE BEGIN 2 */
BSP_SDRAM_Init();
*((uint32_t*)SDRAM_DEVICE_ADDR)=0x12345678;
value=*((uint32_t*)SDRAM_DEVICE_ADDR);
/* USER CODE END 2 */
5.1

## Slide 40: 5.2 BSP LCD lab

## Slide 41: Use BSP for LCD init and writing
Objective
  Learn how import BSP LCD into project
  Because the LCD use the SDRAM we use project from lab 25
  Which part need to by configured in GUI
  Try to write text on LCD
Goal
  Successfully import BSP LCD into your project
  Learn which part you need to import
  How to setup the project
5.2

## Slide 42: Use BSP for LCD init and writing
BSP LCD organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
5.2

## Slide 43: Use BSP for LCD init and writing
BSP LCD organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
1. include stm32f4xx_discovery_lcd.h
stm32f4xx_hal_sdram.c
Utilities
Fonts
2. stm32f4xx_discovery_lcd.h use the discovery BSP and SDRAM
5.2

## Slide 44: Use BSP for LCD init and writing
BSP LCD organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
3. stm32f4xx_discovery_lcd.h use driver ili9341.c which is TFT LCD controller
stm32f4xx_hal_sdram.c
Utilities
Fonts
4. stm32f4xx_discovery_lcd.h use LCTD controller from HAL
5.2

## Slide 45: Use BSP for LCD init and writing
BSP LCD organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
2. stm32f4xx_discovery_lcd.h use fonts from utility folder
5.2

## Slide 46: Use BSP for LCD init and writing
We use the project from BSP SDRAM because the LCD also use the SDRAM
We need copy the Fonts from Utilities folder in CubeMX repository
5.2

## Slide 47: Use BSP for LCD init and writing
The copy part
  In our project in Drivers folder create folder Utilities
  Now go into CubeMX repository …\STM32Cube_FW_F4_V1.3.0\Utilities\
  And copy Fonts into Utilities folder
Copy folders into Utilities
5.2

## Slide 48: Use BSP for LCD init and writing
We add the driver for LCD from HAL
Right click on STM32F4xx_HAL_Drive>ADD from \Drivers\STM32F4xx_HAL_Driver\Src
  stm32f4xx_hal_ltdc.c
  Stm32f4xx_hal_dma2d.c
5.2

## Slide 49: Use BSP for LCD init and writing
We add the driver for BSP LDC
Right click on BSP>ADD from \Drivers\BSP\STM32F429I-Discovery\
  stm32f429i_discovery_lcd.c
Right click on BSP>ADD from \Drivers\BSP\Components\ili9341\
  ili9341.c
5.2

## Slide 50: Use BSP for LCD init and writing
Now last thing is allow to include new HAL files which we added
  Open stm32f4xx_hal_conf.h in ..\Inc\
  Uncomment files which we added
  HAL_DMA2D_MODULE_ENABLED
  HAL_LTDC_MODULE_ENABLED
5.2

## Slide 51: Use BSP for LCD init and writing
Into main.c now we modify include from stm32f429i_discovery_sdram.h to stm32f429i_discovery_lcd.h
And remove the BSP_SDRAM_Init()
/* USER CODE BEGIN Includes */
#include "stm32f429i_discovery_lcd.h"
/* USER CODE END Includes */
/* USER CODE BEGIN 2 */
/* USER CODE END 2 */
5.2

## Slide 52: Use BSP for LCD init and writing
Simple LCD demonstration
/* USER CODE BEGIN 2 */
BSP_LCD_Init();//init LCD
//set the layer buffer address into SDRAM
BSP_LCD_LayerDefaultInit(1, SDRAM_DEVICE_ADDR);
BSP_LCD_SelectLayer(1);//select on which layer we write
BSP_LCD_DisplayOn();//turn on LCD
BSP_LCD_Clear(LCD_COLOR_BLUE);//clear the LCD on blue color
BSP_LCD_SetBackColor(LCD_COLOR_BLUE);//set text background color
BSP_LCD_SetTextColor(LCD_COLOR_WHITE);//set text color
//write text
BSP_LCD_DisplayStringAtLine(2,"Cube STM32");
BSP_LCD_DisplayStringAtLine(3,"BSP");
BSP_LCD_DisplayStringAtLine(4,"LCD DEMO");
/* USER CODE END 2 */
5.2

## Slide 53: www.st.com/stm32